## Slide 1: Sigi IP selection report - LPDDR5 solution
沈君成 shenjc
2021/04/17
上海芯片研发部-芯片设计

## Slide 2: 0. J6 PRD for DDR solution 1. DDR controller key specs and features 2. DDR controller PPA 3. DDR controller AP status 4. DDR PHY key specs and features 5. DDR PHY PPA 6. DDR PHY AP status 7. Conclusions & Thoughts

## Slide 3: J6 PRD for DDR solution
No. | Item | Spec | Cadence | Synopsys | Note
SIGIRIYA-DDR-1 | Data width | 256 bits | √ | √ | SoC should implement multiply DDR solutions to achieve 256 bits data width
SIGIRIYA-DDR-2 | LPDDR5/4X/4 | 6400 / 4266 | √ LPDDR4 only @5500 Mbps | √ | Optional: LPDDR5X support; LPPDR4 low priority confirmed with Terry on 210412 Cadence PHY does not support LPDDR4 for 6400Mbps PHY
SIGIRIYA-DDR-5 | Configurability | Can be switched off for different SKUs | - | - | This feature is not within DDR solution scope and is reliant on SoC logic.
SIGIRIYA-DDR-6 | ECC | Support for inline-ECC | √ | √ | 
SIGIRIYA-DDR-9 | Slew rate and drive strength | Configurable | √ | √ | 
N/A | Data compression | Data compression for codec, GPU, display and camera | - | - | This feature is not within DDR solution scope and may need support from other 3rd party IPs or in-house IPs.

## Slide 4: DDR controller key specs and features
Vendor | Cadence | Synopsys
PRD Protocols | LPDDR5/4/4X | LPDDR5/4/4X
Max data rate (LP5) | 6400 Mbps | 6400 Mbps
Supported ranks | 1, 2, 4 1 | 1, 2
Supported DRAM bits | 16, 32, 64 | 16, 32
Hardware DFS | No | No
Data ports | AXI, CHI, DEN 2 | AXI, HIF 2
Reg interface | AXI, AHB, DEN 2 | APB
DRAM BIST | Yes | No
Automotive features | Inline-ECC; Address parity; On-chip data ECC; Register parity; Key FSM and module duplication. | Inline-ECC; Address parity; On-chip data ECC; Register parity; Key FSM and module duplication.
Note:
1. 4 rank may be supported. Information request sent out on April 2nd but not confirmed yet;
2. DEN and HIF are non-standard and proprietary interfaces.

## Slide 5: DDR controller PPA
Configs | Cadence | Synopsys
Lithography | TSMC 7 nm | TSMC 7 nm
Protocol | LPDDR5/4/4X | LPDDR5/4/4X
Operating frequency | 800 MHz | 800 MHz
Data rate (LP5) | 6400 Mbps | 6400 Mbps
AXI ports | 8 | 2
Number of ranks | 2 | 2
Supported DRAM bits | 32 | 32
CAM entries | 32 | 32
Automotive features | Inline-ECC; Address parity; On-chip data ECC; Register parity; Key FSM and module duplication. | Inline-ECC; Address parity; On-chip data ECC; Register parity; Key FSM and module duplication.
Leakage power | Not provided 1 | Not provided 2
Dynamic power | Not provided 1 | 141 mW, 25% toggle rate, TT 25℃
Area | ≈548,000 um2 | 390,425 um2
1. Information request sent out on April 2nd but not confirmed yet;
2. Synopsys did not record leakage power during evaluation.

## Slide 6: DDR controller AP status
Vendor | Cadence | Synopsys
ASIL design target | B/C | B
ASIL B ready | No ASIL cert for LPDDR5, needs SoW B/C ready for LPDDR4 protocol only | ASIL B ready for 2 typical configs. Non standard config needs SoW.
ASIL B compliant | SoW. No current customer. Vendor is confirming schedule internally. | Scheduled at the end of 2021 for 2 typical configs
ASIL D compliant | SoW. No current customer. Vendor is confirming schedule internally. | SoW. No current customer. Vendor is confirming schedule internally.
Automotive customer design in | Renesas 1 | 芯驰, Mobileye
Automotive customer mass production | No info | 2022
Maturity comparison | 1. DDR solution yearly revenue: Cadence is ~ half of Synopsys; 2. Cadence 64 bits solution is mostly used for DDR5 in datacenters and has not been used for LPDDR5 by any customers. 3. Synopsys claims that ‘All ADAS customers choose our solution.’ | 
1. For MCU, not ADAS

## Slide 7: DDR PHY key specs and features
Vendor | Cadence | Synopsys
PRD Protocols | LPDDR5/4X or LPDDR5/4/4X | LPDDR5/4/4X
Max data rate (LP5) | 6400 Mbps or 5500 Mbps | 6400 Mbps
Supported DRAM bits | 16, 32, 64 1 | 16, 32
DFS frequency targets | 3 | 2
Training | PHY independent HW & SW | PHY independent Binary firmware
Metal stack | 1P13M_2X1Ya5Y2Yy2R_UTRDL 2 | 13M_1X_h_1Xa_v_1Ya_h_5Y_vhvhv_2Yy2R 2
Reg interface | APB, DEN or via controller | APB
ESD | CDM = 8 A@600 V, HBM = 2.5 kV | CDM = 6 A@250 V, HBM = 2 kV
Note:
64 bits needs double row.
Consulted with backend, these two identifiers mean the same metal layer structure.

## Slide 8: DDR PHY PPA
Configs | Cadence | Synopsys
Lithography | TSMC 7 nm | TSMC 7 nm
Protocol | LPDDR5/4X | LPDDR5/4/4X
Data rate (LP5) | 6400 Mbps | 6400 Mbps
Supported DRAM bits | 32 | 32
100% write power | 793 mW | 439 mW
100% read power | 690 mW | 338 mW
Idle power | 129 mW | 157 mW
Area | 2.69 mm2 (3.03 mm2 @5500Mbps if LPDDR4 is needed) | 2.30 mm2 (1.774 mm2 for hard macros) 1
Note:
Synopsys only provides area for hard macros, while PUB soft digital logics and spacing are not considered. The full area of Synopsys PHY will approximately see a 30% increase, according to J5 data. (3.72 mm2 full PHY TOP vs 2.875 mm2 hard macros).
Cadence power is noticeably higher. Confirmation request sent out, still waiting for response.

## Slide 9: DDR PHY AP status
Vendor | Cadence | Synopsys
AEC Q100 | No official grade; Signoff -40 ~ 125 ℃; ESD passed; | Grade 2
ASIL design target | SoW. No customer. Vendor is confirming schedule internally. | B
ASIL B ready | SoW. No customer. Vendor is confirming schedule internally. | ASIL B ready
ASIL B compliant | SoW. No customer. Vendor is confirming schedule internally. | Scheduled at the end of 2021
ASIL D compliant | SoW. No customer. Vendor is confirming schedule internally. | SoW. No customer. Vendor is confirming schedule internally.
Automotive customer design in | Renesas | 芯驰, Mobileye
Automotive customer mass production | No info | 2022
Maturity comparison | 1. Both have test chip for 6400 Mbps 32 bit 2 ranks @ TSMC 7 nm; 2. Cadence 64 bit PHY has not been taped out; 3. Both have customer designed-in; 4. Cadence DDR PHY is not an automotive product; Needs custom-built for AP; Schedule pending. | 

## Slide 10: Conclusions & Thoughts
Vendor | Cadence | Synopsys
Pros | Controller has support for DRAM BIST; Controller and PHY use a universal register interface; Native support for CHI interface. More user-friendly deliverables: SDC hierarchy, reference C code; More frequency targets for DFS. May be able to use 64 bits. | Can inherit and reuse experience from previous project as much as possible; ASIL B ready for 2 typical configs; ASIL B compliant at the end of 2021; Better PPA. More automotive customers.
Cons | 6400 Mbps PHY does not support LPDDR4. PHY is not AP; Controller does not have ASIL ready for LPDDR5 but only for LPDDR4; Worse PPA. | Weird PHY register interface (16 bit APB, none standard addressing); Not so user-friendly: No SDC hierarchy. No reference C code; Long response time for support requests; Only two frequency targets for DFS. No DRAM BIST. Horizon in-house design might be risky and requires considerable efforts.